## Slide 1
SMB Version 2: Scaling from Kilobits to Gigabits
Jim Pinkerton & Thomas Pfenning
File Access and Distribution, Storage Systems Division
Microsoft Corporation
18. April 2008

## Slide 2: Agenda
Introduction
SMB Version 2 Design goals
WAN Characteristics
Performance comparisons
  Layering & Bottlenecks
  Test environment
  Test Results
Questions

## Slide 3: Introduction
SMB legacy from 1983
  SMB/CIFS: SMB -> CIFS -> SMB -> SMBv2
  CIFS = SMB as it shipped in NT4 server
  Windows 2000 and later
    Kerberos and domains
    Shadow copy
    Server – to – Server copy
    SMB signing
Trends
  Proliferation of branch offices
  Server consolidation and virtualization
  Mobile workers
  WAN accelerators

## Slide 4: SMB Version 2 Design goals
Opcode complexity
  SMB > 100 vs. SMB v2 = 19
  Extension mechanism (eg. create context, variable offsets)
Symbolic Links
More Flexible compounding
  Parallel or chained
  Response for every element in the chain
Durable Handles
  Reconnect on loss of connection
Crediting mechanism for the # of outstanding operations
  Resource control for clients
  Fill underlying pipe
Increased scalability for large servers
  E.g. fileid 64 bit, sessionid 64 bit, treeid 32 bit, shareid 32bit
Async operations are treated completely separately
Improved Signing security
  HMAC SHA-256 vs. MD5
NAT Friendliness
  VC count is gone

## Slide 5: Network Characteristics
Network Media link speed spans 10^6
  Cellular modems
  Dial-Up networking 9600, 19200 Baud
  Remember PC network 2Mb/s and Token Ring 4Mb/s?
  10Mb/s – 1Gb/s Ethernet
  10GBE and 16Gb/s Infiniband
Latency
  <1ms to 1200ms
Anandeep

## Slide 6: Corporate Network Characteristics
Continental Latencies (ms)
Intercontinental Latencies (ms)
 | North America | Europe | Asia
Mean | 108 | 109 | 163
Stddev | 69 | 91 | 81
Min | 20 | 5 | 20
Max | 375 | 372 | 460
 | North America | Europe | Asia | South America
Mean | 311 | 466 | 415 | 615
Stddev | 81 | 83 | 138 | 48
Min | 110 | 135 | 91 | 188
Max | 655 | 717 | 830 | 1256
Data Centers in the US, Europe and 2 in Asia
  ICMP Pings on quiet networks

## Slide 7: Corporate Network Characteristics
Continental Bandwidth (Mb/s)
Branch Distribution (ms)
 | North America | Europe | Asia | South America
Mean | 14 | 33 | 26 | 5.5
Stddev | 28 | 43 | 28 | 7.2
Min | 1.3 | 0.9 | 3.5 | 0.5
Max | 155 | 155 | 92 | 25

## Slide 8: Corporate Network Characteristics
Continental BDP (MB)
Intercontinental BDP (MB)
Bandwidth Delay Products
  # of outstanding SMB requests required to fill a pipe
 | North America | Europe | Asia
Mean | 0.21 | 0.25 | 0.53
Stddev | 0.45 | 0.30 | 0.46
Min | 0.008 | 0.005 | 0.083
Max | 2.80 | 1.60 | 1.80
 | North America | Europe | Asia | South America
Mean | 0.71 | 2.40 | 1.70 | 0.46
Stddev | 1.40 | 3.00 | 1.60 | 0.58
Min | 0.05 | 0.08 | 0.27 | 0.06
Max | 6.60 | 11.00 | 5.90 | 1.90
Denmark – Singapore: 155Mbit/s with 592ms delay results in 11MB BDP
Recent MAN result: 1Gbit/s with 76ms delay results in 9.5MB
…. ~50MB in the near future

## Slide 9: Optimizing for WAN
For low speed WAN links
  Small SMB PDU
    Better responsiveness for mix of file transfers and directory enumeration
  Limit outstanding data
    Avoid false I/O timeouts due to head-of-queue blocking
For high speed WAN links
  Scale the BDP
    Each layer in the stack has a roll
  Ensure congestion doesn’t tank performance
This talk will examine copying a file from a local disk to a remote disk to show all the layers involved
The Client Layers
Directly affects BDP
Affects end-to-end perf
CopyFiIeEx
IO Manager
SMB2
TCP
Robocopy
Xcopy
Drag-N-drop
Network
NTFS
SCSI
Synchronous
Async
Kernel
User Mode
9

## Slide 10: TCP Layer Optimizations for WAN
Feature | Vista RTM | Windows 2008
Receive Window auto-tuning | Yes (up to 16 MB, wininet 256 KB) | Yes (up to 16 MB)
CTCP | N (default) | Y
Old Congestion Control | Y | N (default)
RFC 3540 - ECN | N (default) | N (default)
RFC 3782 - NewReno | Y | Y
RFC 2883 – SACK extensions | Y | Y
RFC 3517 – SACK based loss recov. | Y | Y
RFC 4138 – Forward RTO recovery | Y | Y
On Windows, can be enabled/disable the following with netsh commands:
CTCP
ECN
Autotune receive window up to 1 GB (experimental)
Optimization categories:
Congestion (lots of issues)
Scale receive window from a small value to something quite large
10

## Slide 11: SMB2 Tuning for low speed links
Goals:
  Attempt to maintain application responsiveness
  Attempt to not cause false timeouts on I/Os
Algorithms:
  Timer is armed when SMB packet is sent – not when application posts I/O.
  Server ramps from a small number of credits to Smb2MaxCredits
    Starts at 16, scales to 128
  Throttling credits as a function of bandwidth
  Dynamically vary PDU size (see below)
    Struct that dynamically modifies PDU size by measured link speed:
    static ULONG BufferSizeBuckets[] = {
    0x4000, // 0: 0-64 Kbps 16 KB
    0x4000, // 1: 64-128 Kbps
    0x8000, // 2: 128-192 Kbps 32 KB
    0x8000, // 3: 192-256 Kbps
    0x10000, // 4: 256-320 Kbps 64 KB
    0x10000, // 5: 320-384 Kbps
    0x10000, // 6: 384-448 Kbps
    0x10000, // 7: 448-512 Kbps
    0x10000 // 8: > 512 Kbps
    };
11

## Slide 12: CopyFileEx Optimizations for WAN
Balance of:
  Virtual Address pressure (32 bit OS)
  Non-paged pool (kernel pinned memory)
  Filling the BDP
  Keeping under 64 KB for read for SMB1 so don’t end up with 2 PDUs
File Size | Pipeline Depth | Chunk Size
<= 1MB | 1 | File size rounded to sector size
> 1MB and <= 8 MB | 2 | 1 MB
> 8 MB and <= 256 MB | 4 | 2 MB
> 256 MB | 4 | 8 MB
File Size | Pipeline Depth | Chunk Size
<= 512kB | 8 | 128kB
> 512kB and <= 2 MB | 8 | 256 kB
> 2 MB and <= 8 MB | 8 | 512kB
> 8 MB | 8 | 1 MB
Vista RTM, For SMB2
Vista SP1, For SMB2
XP(SMB1)
Synchronous 64 KB Writes
Synchronous 60 KB Reads
Vista SP1 (SMB1)
Multiple async 32 KB Writes, 16 chunks
Multiple async 32 KB Reads, 16 chunks
12

## Slide 13: Testing WAN
Focus:
  Create reliable test infrastructure with very tight variance so that small performance regressions are real (and can be automatically detected)
    Need to take disks out of the equation – use a RAM disk instead
    Tolerances for even smallish I/Os are pretty tight (<1-2%)_
Hardware:
  2 hosts
  1 gigabit LAN, h/w WAN simulator (vary only latency for now)
  64 bit hardware, Intel Xeon, dual core, 1.6 GHz
  4 GB RAM (1.2 GB RAM disk)
  Boot disk on SATA
Software:
  Windows XP (64 bit) on SMB1 client, Windows Server 2003 (64 bit) on SMB1 server
  Vista SP1 (64 bit) on SMB2 client, Windows Server 2008 (64 bit) on SMB2 server
Qualifications:
  BECAUSE THIS USES A RAM DISK, THEY ARE “BEST CASE” – i.e. never to be seen in the field
  Test infrastructure is brand new – still being sanity checked
  Plan is to submit a paper for the SNIA Fall SDC with full data
13

## Slide 14: Local to Remote RAM Disk
Test details:
  SMB1 is Windows XP
  SMB2 is Vista SP1
  WAN emulator for 2 ms, 100 ms
  Direct connect for 0 ms
  Single outstanding filecopy (i.e. not multiple files)
Observations:
  100 ms, 1 gig, not scaling
  Filecopy on SMB1 on XP had serious issues with even 2 ms latency (let alone 100)
    Filecopy had single ~60KB buffer outstanding
  Filecopy/Credits/TCP scaling algorithm needs further tuning (100ms climbs very late)
Chart: CopyFile(L->R), Varying Latency, File Size, SMB1/2
| 1 | 4 | 8 | 32 | 64 | 256 | 512 | 1000 | 2000 | 4000 | 8000 | 32000 | 64000 | 256000 | 512000 | 1000000
SMB1 (0ms added RTT) | 4044.4894 | 15992.004 | 29822.9264 | 112231.4774 | 184040.2588 | 389649.9239 | 489425.2599 | 538358.0081 | 584581.6588 | 607833.4536 | 621359.2233 | 613026.8199 | 599672.0543 | 529746.508 | 507684.6802 | 527746.2596
SMB2 (0ms added RTT) | 2391.6293 | 10217.1137 | 20031.2989 | 73796.4831 | 132676.8593 | 333931.1919 | 438309.2563 | 509229.7899 | 561797.7528 | 593471.8101 | 675747.0172 | 759193.3571 | 789879.6668 | 822820.4098 | 836088.9978 | 829273.3492
SMB1 (100ms added RTT) | 9.9416 | 39.7466 | 79.4439 | 317.5391 | 563.6904 | 1684.2105 | 2519.0652 | 3142.1838 | 3731.3433 | 4097.3111 | 4344.8744 | 4514.195 | 4547.0693 | 4559.2164 | 4565.8232 | 4456.8245
SMB2 (100ms added RTT) | 15.2178 | 60.8365 | 121.5113 | 485.4001 | 971.1684 | 3863.422 | 7679.0401 | 14831.294 | 29011.786 | 55420.8521 | 92874.7642 | 260905.0143 | 221549.1129 | 239588.2078 | 239953.1342 | 253646.1636
SMB1 (2ms added RTT | 363.1412 | 1440.7924 | 2787.4564 | 10898.2546 | 19233.6589 | 49456.653 | 68817.2043 | 81682.6629 | 91272.105 | 97620.5003 | 101458.4654 | 103101.0874 | 103455.2435 | 103748.7335 | 103669.957 | 101394.1698
SMB2 (2ms added RTT) | 498.132 | 1969.2308 | 3753.6657 | 14772.0716 | 29173.7892 | 101335.9723 | 173780.2291 | 269450.9936 | 378519.0442 | 475907.1981 | 598690.3648 | 730385.1641 | 781321.5321 | 825473.5994 | 833028.2693 | 830909.8463
RAM DISK USED – DO NOT QUOTE THESE NUMBERS

## Slide 15: Bottlenecks: Scaling BW for Smaller Files in Latency Tolerant Way
Observations
Additional latency requires larger files before start of climbing BW curve (as expected)
Slope changes substantially at 64 KB
  Prefetch/full disk reads kick in
  SMB2 pipelining kicks in
Slope changes substantially at 4 MB
  CopyFileEx 512 KB buffers, going to 1 MB for > 8 MB
Chart: CopyFile(L->R), SMB2 Varying Latency, File Size
| 1 | 4 | 8 | 32 | 64 | 256 | 512 | 1000 | 2000 | 4000 | 8000 | 32000 | 64000 | 256000 | 512000 | 1000000
SMB2 (0ms added RTT) | 2391.6293 | 10217.1137 | 20031.2989 | 73796.4831 | 132676.8593 | 333931.1919 | 438309.2563 | 509229.7899 | 561797.7528 | 593471.8101 | 675747.0172 | 759193.3571 | 789879.6668 | 822820.4098 | 836088.9978 | 829273.3492
SMB2 (100ms added RTT) | 15.2178 | 60.8365 | 121.5113 | 485.4001 | 971.1684 | 3863.422 | 7679.0401 | 14831.294 | 29011.786 | 55420.8521 | 92874.7642 | 260905.0143 | 221549.1129 | 239588.2078 | 239953.1342 | 253646.1636
SMB2 (2ms added RTT) | 498.132 | 1969.2308 | 3753.6657 | 14772.0716 | 29173.7892 | 101335.9723 | 173780.2291 | 269450.9936 | 378519.0442 | 475907.1981 | 598690.3648 | 730385.1641 | 781321.5321 | 825473.5994 | 833028.2693 | 830909.8463
RAM DISK USED – DO NOT QUOTE THESE NUMBERS

## Slide 16: Bottlenecks: Max Credits and Bandwidth Throttling
Observations
RTM bits top out at ~250 mb/s
Removing credit throttling due to BW estimation moves to ~500 mb/s
Removing credit throttling and increasing credits to 512 moves to ~800 mb/s
Chart: CopyFile(L->R), SMB2 Varying Latency, File Size, Algor.
| 1 | 4 | 8 | 32 | 64 | 256 | 512 | 1000 | 2000 | 4000 | 8000 | 32000 | 64000 | 256000 | 512000 | 1000000
SMB2 (100ms) | 15.2178 | 60.8365 | 121.5113 | 485.4001 | 971.1684 | 3863.422 | 7679.0401 | 14831.294 | 29011.786 | 55420.8521 | 92874.7642 | 260905.0143 | 221549.1129 | 239588.2078 | 239953.1342 | 253646.1636
SMB2 (100ms no credit throttle) | 15.212 | 60.8365 | 121.5344 | 485.6763 | 902.839 | 7417.6023 | 28050.4909 | 92820.8847 | 348773.842 | 496725.6852
SMB2 (100 ms no throttle, 512 credits) | 15.2062 | 60.7556 | 121.4421 | 485.5842 | 969.8807 | 3861.9649 | 7680.48 | 14853.3234 | 29006.5265 | 55836.6777 | 102057.0882 | 281318.6813 | 418300.6536 | 666666.6667 | 743645.6064 | 778967.8676
RAM DISK USED – DO NOT QUOTE THESE NUMBERS

## Slide 17: SMB Future Evolution
  Documentation and interoperability
  Performance
    Improved bandwidth scaling with all components together
      BW estimation, more rapid credit scaling, TCP rcv window growth
    HPC workloads
    Larger SMB PDUs
    Better branch performance
    Small file throughput
    Chattiness
    Oplocks
  Better Unix interop
  Unique Implementation ID
  Encryption
  Compression
  FAN
  Clustering
  Server workloads
  Not ordered by priority or committed!